## Slide 1: Internship at UFRGS
Chirp Detection 14/08/2014

## Slide 2: Principle
Acoustic beacon
Robot
Auto-calibration
Auto-calibration
send chirp
receive chirp
send chirp
receive chirp
Measuring time of flight

## Slide 3: What is a chirp ?
A signal in which the frequency increase or decrease with time.

## Slide 4: Why is chirp used ?
Compared to mono-frequency impulsion :
  Increasing the length of impulsion decrease the precision of detection

## Slide 5: Why is chirp used ?
Compared to mono-frequency impulsion :
  Chirp has a better noise-resistance

## Slide 6: Operation
On the robot side :
  Start Recording ambient sound
  Send Chirp
    Hear its own chirp
    Hear the beacon chirp
  Calculate the time between the two chirp
On the beacon side :
  Start Recording ambient sound
    Hear the robot chirp
  Send chirp 1 second later (exactely)

## Slide 7: Challenge with time-measuring
Speed of sound :
  330 m/s in the air ( 33 cm for 1 ms)
  1500 m/s in water (1.5 m for 1 ms)
Source of imprecision :
  Latency in sound card
  The intern clock cannot be trusted
    Using fonction such as time.time() is impossible

## Slide 8: A solution: using the number of frames
Sound card is set on non-blocking mode :
  Creates a new thread to control the sound card
  Always recording
  The rate is known and precise
This solution solves the problem of latency (for the robot)
Number of frames
Peak on speaker
Time of detection
Output Latency
Input Latency
Delay to measure
Total Latency

## Slide 9: Source of vagueness
Autocalibration is needed for the beacon
  Must send back chirp 1 sec later
Number of frames
Peak on speaker
Time of detection
Output Latency
Input Latency
Must be 1 sec
1 second less total latency

## Slide 10: Operating principle
4 object:
  Callback fonction : record the sound
  FIFO : store the data
  Chirp detection: detect the chirp
  Semaphore : which regulate the use of the FIFO

## Slide 11: Operating principle
  Callback
  FIFO
  Chirp detection
  Semaphore
Detection
Size of a chirp

## Slide 12: Nowadays
Using pyAudio to access the sound card
Software works great on Windows
  Accurate to 40 centimeter
Does not work on raspberrypi or Linux
  Configuration of the sound card is very difficult
  Latency varies with time
  Not stable (stop working after multiple test)